## Slide 1: Bluetooth

## Slide 2: Bluetooth
A wireless standard (like WiFi) designed for point-to-point communication
Primary applications
  Connect peripheral devices (mouse, keyboard, headphones, fitness trackers)
  Radio Frequency Identification (RFID)
Maximum range of ~100m
Two types (same range:
  Bluetooth Classic
    Designed for higher-throughput connections such as audio
    Persistent wireless connection (radio stays on)
  Bluetooth Low Energy (BLE) (what we’ll use)
    Designed for low-throughput, low-power connections
    Radios connect at negotiated intervals for short bursts

## Slide 3: Advertising
Bluetooth device broadcasts its address and some advertising payload data (configurable) at a regular rate (e.g. every 1s)
  Very low power usage (uA)
Key component to RFID
  Received Strength of Signal Indicator (RSSI) - dBm
  AirTag, Tile primarily work this way (also now ultra wide band)

## Slide 4: Advertising on the M5StickCPlus (ESP32)

## Slide 5: Bluetooth in Python via Bleak
Bleak is a modern, cross-platform python library for BLE
  Uses “asynchronous” programming features of python, which allow events to be “awaited” within async functions
  Requires an “event loop” to run (asyncio.run) … more on this later
pip install bleak

## Slide 6: Doing More with GATT Profiles
If we connect to a device, we can send/receive data
Generic ATTribute Profile
  Consists of services, which consist of characteristics
  Services attempt to standardize how to communicate with a device class
  Characteristics are ultimately what is used to transmit and receive data
See https://learn.adafruit.com/introduction-to-bluetooth-low-energy/gatt?view=all for a more in-depth explanation

## Slide 7: Characteristics
UUID - Universally Unique ID (https://www.uuidgenerator.net/)
Properties
  Read - Value can be read by a client on demand (polling, e.g., what is the temperature?)
  Write - Value can be written by a client on demand (e.g., set the motor to this speed)
  Notify/Indicate - Updated values are automatically sent to the client (e.g., this is the new value of the accelerometer)
    Only when enabled by the client
Value
  Usually, <= 20 bytes of data
  Newer version of Bluetooth (4.2+) allow for more by changing the Maximum Transmission Unit
Descriptors
  Hold useful information about the characteristic (e.g., name), and may be read/written depending on the type
  Notify/Indicate require a special writable descriptor (0x2902) called the CCCD (client characteristic configuration descriptor)

## Slide 8: Connection Intervals and Data Rates
BLE normally uses a data rate of 1Mbps at the “link” layer (operates on 2.4Ghz spectrum)
  In practice, less, because of protocol overhead.
Client and Server only connect to each other so often to exchange data
  Minimum and maximum values, between 7.5ms and 4s
  Negotiated by client and server
  Higher is better to reduce power consumption
Several packets may be sent each connection
  Varies by device, interference

## Slide 9: Minimal Bluetooth M5Stick (1 characteristic)

## Slide 10
Note the use of threads, which allows you to mix in other event loops

## Slide 11: Bluetooth or WiFi?
WiFi is generally better, if it’s available
  Much more bandwidth available
  Multiple devices can communicate with each other
But you may already be using your WiFi radio to connect to the internet
  Also, the other device might not have WiFi
Bluetooth is normally used for devices that can be used anywhere, in an ad hoc manner
M5StickCPlus is not the most power-efficient Bluetooth sensor (better as the “central”)